## SWPPP for Municipal Operations NOI

POTENTIAL POLLUTANTS AND ACTIVITIES

Potential Pollutants released from MTSU activities.

Activity Potential Pollutants

GLOSSARY OF TERMS

Biochemical oxygen demand – Depletion of dissolved oxygen in water caused by decomposition of chemical or biologic matter.

Catch Basin – A unit that is installed to capture and retain debris, particulate matter, or other solid materials, but allows stormwater to “flow through” to its discharge location

Drip Irrigation –irrigation via a perforated device (i.e. hose) that allows for a slow watering method with reduced evaporation and runoff losses

Hydraulic – Referring to water

Loading – Term used in conjunction with sediment and hydraulic to describe excessive amounts (of the term that is described)

Naturescaping – An alternative landscaping technique that incorporates native plants and creates beneficial wildlife habitat – also conserves water and energy, reduces soil/water pollution.

Oil/Water Separator – A unit that is installed “in line” to a wastewater discharge pipe which is devised to capture petroleum derived materials that float on water

Pesticides – Products that are toxic and are used to kill pests - can be classified as insecticides, herbicides, rodenticides, biocides, and aquacides.

Sediments - Small particles of matter that settle to the bottom of a body of water

Silt – Material consisting of mineral soil particles ranging in diameter from 0.02 millimeters to 0.002 millimeters

Stormwater - rainwater runoff or snow melt waters – these waters can interact with different types of materials, transporting contaminants to surface waters (i.e. streams, creeks, rivers)

Toxicity –The relative degree of being poisonous

Zero input, low input (lawns) - have minimal need for care (i.e. addition of fertilizers/pesticides, water, etc.)

VEHICLE/EQUIPMENT MAINTENANCE

POLLUTION PREVENTION/GOOD HOUSEKEEPING PRACTICES

1. IDENTIFY IMPACTS TO STORMWATER/RECEIVING WATERS

Trace amounts of metals/hydrocarbons are found in materials (i.e. fuels, antifreeze, batteries, motor oils, grease, parts cleaning solvents) that are typically used in maintenance operations

2. PROBLEM EVALUATION: IMPACT ON RECEIVING WATERS,

PRIORITIZE

Toxicity

Biochemical oxygen demand

3. IDENTIFY SOLUTIONS (BMPs)

Conduct maintenance work indoors – if work must be performed outside, guard against spillage of materials that could discharge to storm receivers

Make sure floor drains flow to sanitary sewer and install pretreatment systems (oil/water separators) where necessary in sewer lines to capture contaminants (oil, grit), and maintain as needed

Clean up spilled materials immediately, using “dry” methods

Never leave vehicles unattended while refueling

Identify appropriate recycling/disposal options for wastes

4. INSPECTION PROCEDURES

Inspect (for maintenance purposes) floor drain systems, oil/water separators

Monitor “parked” vehicles/equipment for leaks

5. MAINTENANCE PROCEDURES

Map storm drain locations accurately to avoid illegal discharges

Maintain a clean work area – remove contaminants from floors, drains, catch basins, using “dry” methods

Repair or replace any leaking containers

Use steam cleaning /pressure washing instead of solvent for parts cleaning

Store waste fluids in properly capped, labeled storage containers

Store batteries in leak-proof, compatible (i.e. non reactive) containers

Rinse grass from lawn care equipement and scoop up debris and put in trash – no grassy areas near water source

Protect against pollution if outside maintenance is necessary (cover storm receivers; use secondary containment vessels, etc.)

Measure effectiveness – Monthly Preventive Maintenance (PM) in work order system

6. ADVISORY

Report petroleum spills (as necessary) to the MTSU EH&S department.

VEHICLE/EQUIPMENT WASHING

POLLUTION PREVENTION/GOOD HOUSEKEEPING PRACTICES

1. IDENTIFY IMPACTS TO STORMWATER/RECEIVING WATERS

Nutrients (biodegradable soaps)

Metals

Hydrocarbons

Grease

Oils

2. PROBLEM EVALUATION: IMPACT ON RECEIVING WATERS

Biochemical oxygen demand from nutrient sources

Toxicity

3. IDENTIFY SOLUTIONS (BMPs)

Initiate single purpose use of vehicle bays - dedicate only one bay for washing (with floor drain system)

Perform cleaning with pressurized cold water, without the use of soaps, if

wastewaters will flow to a storm sewer system when applicable

Rinse with hoses that are equipped with automatic shutoff devices and spray nozzles when applicable

Filters to be added to new construction when available

Mount spill kits to contain and treat all spills

4. INSPECTION PROCEDURES

Inspect floor drain systems regularly - use only those that discharge to a sanitary sewer, identify the need for cleaning of catch basins, oil/water separators

Inspect catch basin inserts or berms and clean them regularly

5. MAINTENANCE PROCEDURES

Map storm drain locations accurately to avoid illegal discharges

Perform pressure washing where wastes can be captured forproper disposal

Take precautions against excess use of/spillage of detergents

Document cleaning of filters

6. ADVISORY

Require all facilities to connect floor drain systems to sanitary sewers (if available)

VEHICLE/EQUIPMENT FUELING

POLLUTION PREVENTION/GOOD HOUSEKEEPING PRACTICES

1. IDENTIFY IMPACTS TO STORMWATER/RECEIVING WATERS

Fuel

Heavy metals

2. PROBLEM EVALUATION: IMPACT ON RECEIVING WATERS,

PRIORITIZE

Biochemical oxygen demand from nutrient sources

Toxicity

3. IDENTIFY SOLUTIONS (BMPs)

Fueling areas should be covered

Have a spill prevention plan

Mount spill kits to contain and treat all spills

Never leave vehicles unattended while refueling

4. INSPECTION PROCEDURES

Inspect regularly for corrosion and structural failure, spills and overfills and failure of any piping systems

Make sure emergency shut off is functioning properly

Inspect overfill spill buckets monthly

TDEC does Underground Storage Tank Inspections regularly

5. MAINTENANCE PROCEDURES

Map storm drain locations accurately to avoid illegal discharges

Dry cleanup methods should be used

Inspect site regularly

Document all TDEC required UST requirements

6. ADVISORY

Report spills to MTSU EH&S department and refer to MTSU SPCC Plan for guidance

OUTDOOR MATERIAL STORAGE

POLLUTION PREVENTION/GOOD HOUSEKEEPING PRACTICES

1. IDENTIFY IMPACTS TO STORMWATER/RECEIVING WATERS

Sediment

Heavy metals

Oil

Stockpile materials (sand, mulch, etc.)

Organics

Oxygen Demanding Substances

2. PROBLEM EVALUATION: IMPACT ON RECEIVING WATERS,

PRIORITIZE

Biochemical oxygen demand from nutrient sources

Toxicity

Hydraulic loading

3. IDENTIFY SOLUTIONS (BMPs)

Stockpile area should be covered when available

Berm area or provide containment to prevent loss of materials

4. INSPECTION PROCEDURES

Inspect regularly for material seepage through berms

Inspect berms for need to cleanup

5. MAINTENANCE PROCEDURES

Map storm drain locations accurately to avoid illegal discharges

Clean up area regularly to prevent illegal discharges

Inspect site regularly

No change to material storage – area bermed so no runoff issues